## Slide 1: PVDOMICS
Chapter 70
Cardiac MRI Testing Overview and General Information
NHLBI Pulmonary Vascular Disease Phenomics Program
Funded by the National Heart, Lung, and Blood Institute of the
National Institutes of Health with support from
the Pulmonary Hypertension Association
Notes: Good afternoon. Today’s training will cover Chapter 70 Cardiac MRI Testing Overview and General Information. Dr. Kwon provides an excellent overview of the required parameters. This presentation is meant as and adjunct to her training session.

## Slide 2: PVDOMICS
A novel NHLBI Network Research Initiative in Pulmonary Vascular Disease established to perform comprehensive phenotyping and endophenotyping in order to define new meaningful sub-classifications of patients with PVD. The long-term goal is utilization ofendophenotypes/biomarkers for early diagnosis, at-risk screening, and personalized approaches for interventions and/or preventions of PVD.
Cardiac MRI Training and Reference
PVDOMICS
2
Notes: As you all know, PVDOMICS expects to define new WHO sub-classifications of patients with PVD and through the study design, identify markers for early diagnosis and possible prevention of PVD

## Slide 3: CV Imaging Core
Christine Jellis
Deborah Kwon
James Thomas
Annitta Flinn
Margaret (Koko) Park
Kathleen Kassimatis
Dawn
D’Eusanio
Cathy McDowell
Jill
Rusticelli
Michelle
Baksar
Jeanne
Drinko
Notes: This is the C5Research Imaging Core Lab Team under the leadership of Drs. Kwon, Jellis and Thomas. You will likely be interacting with other members of the team regularly and thought names and faces would be helpful.

## Slide 4: Goals of Cardiac MRI
Quantify cardiac volume and mass, fibrosis and scarring
Evaluate perfusion and flow
Compare CMR measures of RV performance to advanced echocardiographic measures.
Help determine useful parameters to aid in early detection and reclassification of pulmonary hypertension.
Notes: MRI is the gold standard for RV analysis and diagnostic tool for multiple RV disease states including PVD. The goal of the cardiac MRI, other than those listed, is to capture subtle changes in right sided cardiac function in PAH before hemodynamic decompensation occurs. Thus aiding in early detection , reclassification and possible prevention of PVD.

## Slide 5: Cardiac MRI Processes
Safety
Imaging Schedule
Qualification Exam
Quality Control & Status Reports
Anonymization
Digital Image Transfer (AG Mednet)
Archival Instructions
Data Clarification Process
Replacement/Inactivation Process
Contraindications, Exceptions, Getting Started
Cardiac MRI Protocol and Image Acquisition Instructions
Notes: Skip and Kill slide

## Slide 6: Cardiac MRI Safety Process
Preventive Maintenance (PM) Document
  Prior to Qualification, a copy of the current annual PM document for each CMR scanner planned for use in the PVDOMICS trial, including serial number, must be submitted to the Imaging Core. This satisfies American College of Radiology (ACR) recommendations and ensures the mechanical integrity of the imaging system.
  Sites must follow ACR Safe Practice Guidelines
Notes: We will be reviewing all the Imaging Core Processes. SAFETY is the first. To ensure the mechanical integrity of each scanner planned for use in the trial and in keeping with ACR recommendations copies of annual PM documents have already been requested and will be collected each year for the duration of the trial.

## Slide 7: Cardiac MRI Imaging Schedule
Imaging Visits | Description
Qualification | Submit a qualification CMR to Core Lab before enrollment
Visit | Baseline CMR
Notes: The imaging schedule is simple. Following qualification, only a Baseline study is expected.

## Slide 8: Cardiac MRI Qualification Process
Qualification Cardiac MRI (CMR)
  All sites will submit a de-identified sample of a recently performed CMR exam completed at their institution.
  The purpose of the qualification exam is to ensure viewer and analysis compatibility between the site and Core Lab prior to subject recruitment.
The Qualification process must be completed prior to sites submitting CMR exams of enrolled subjects
Notes: QUALFICATION PROCESS: All sites must submit a de-identified sample of a recently performed cMR exam completed on the scanner planned for use in this trial. The purpose of this is to ensure compatibility between site scanner and ICL analysis tools. We want to be certain we have no problems opening a study prior to site enrollment. Therefore, Qualification is to be completed prior to submission of enrolled subjects.

## Slide 9: Cardiac MRI Qualification Process
AG Mednet
  Is the secure digital transfer service designated for this trial
  The electronic CMR data transmittal form will be completed prior to transfer of the qualification exam (or any exam) to the Imaging Core via AG Mednet.
Qualification Status
  Site and Data Coordinating Center (DCC) will be notified of qualification status via email or fax
Qualification Resubmission
  If the site does not qualify with the first submission, the Imaging Core will make recommendations for resubmission of another CMR Qualification study.
Notes: For Qualification to occur, sites must successfully upload a recently performed CMR through AGMednet, the secure digital image transfer service designated for this trial. Site and DCC will be notified of qualification status via email or fax. If site does not qualify with the first submission, the Imaging Core will make recommendations for resubmission.

## Slide 10: Cardiac MRI Quality Control
CMR Critique
  CMR images will be monitored for quality and adherence to the PVDOMICS imaging protocol.
  The Imaging Core will provide feedback in the form of a critique to sites and the DCC via email for each CMR submitted.
  The critique should be shared with the technologist performing the CMR exam to ensure the acquisition of research quality data and to help prevent the possibility of missing data.
  The critique is a tool intended to standardize the collection of research quality data and to capture mistakes, if any, before they are repeated.
Notes: – READ first second and 3rd points. And should be share with the technologist performing the exam.

## Slide 11: Cardiac MRI Status Reports
Reports
  Inventory/Quality
  Incomplete Cases
  Comprehensive Data Clarification
  Outstanding Data Clarifications
Report Distribution
  Designated sponsor personnel
  Frequency of distribution determined by sponsor
Notes: There are 4 status reports provided by the Imaging Core on a weekly basis to the DCC. They are an Inventory/Quality Report, Incomplete Cases Report, Comprehensive Data Clarification Report and Outstanding Data Clarifications Report. These reports are intended as tools to aid in site management.

## Slide 12: Anonymization Process
Secure study assigned subject ID from site coordinator.
For purposes of confidentiality and to remain compliant with Health Insurance Portability and Accountability Act (HIPAA), all references to a specific subject must be made using the entire Subject ID.
Site is responsible for correctly de-identifying clinical exams with the correct study assigned Subject ID within the AG Mednet application.
Notes: Anonymization Process: HIPAA compliance dictates that all references to a specific subject must be made using the Subject ID. Sites are responsible for correctly de-identifying clinical exams with the correct study assigned Subject ID within the AG Mednet application.

## Slide 13: Digital Image Transfer AG Mednet
AG Mednet is a web-based diagnostic imaging network, enabling sites to send diagnostic image exams electronically and securely to the Imaging Core Lab.
  AG Mednet will provide tools and training to anonymize exams, complete transmittal forms electronically and complete other trial specific tasks.
Download the Cardiac MRI Transmittal Form #251 from the QHS website (http://qhsapps.ccf.org/pvdomics/). The site technologist is responsible for sections 6 through 20; the remaining fields are the coordinator’s responsibility. Completion of this hard copy data transmittal form will aid in the completion of the AG Mednet Electronic Data Transmittal Form prior to exam upload.
Please transfer exams as they are collected.
Notes: As mentioned earlier, AG Mednet is the imaging network enabling sites to send de-identified CMRs electronically and securely to the Imaging Core. AG Mednet will provide tools and training to accomplish this. Download the Cardiac MRI Transmittal Form #251 form the DCC Website.

## Slide 14: Data Transmittal Form: MRI
Sites will enter required demographic data in electronic transfer system
Notes: Please note the Technologist is responsible for sections 6 – 20 (green); remaining fields are the coordinator’s responsibility. Please tx exams as they are collected.

## Slide 15: Archival Instructions
Complete the electronic Data Transmittal Form carefully and completely. This is treated as a source document and is subject to audit by regulatory authorities.
Archive the cardiac MRI scan to digital media (CD/DVD) immediately from the imaging system used to acquire the images prior to archiving to Picture Archiving and Communication System (PACS).
  Make one copy of each CMR exam per disc and upload from this media to the AG Mednet website location. Retain disc copy of exam with site records.
Notes: Complete the electronic Data Transmittal Form carefully and completely. This is treated as a source document and is subject to audit by regulatory authorities. Whenever possible archive …Read slide

## Slide 16: CMR Data Clarification Process
Query Notification
  The study coordinator or designee and the sponsor will receive an email from the Imaging Core asking for resolution of any issues discovered during the quality control (QC) process. Prompt response is required form the site coordinator.
  Query Data Tracking Form
    Review the variable name, reported value and comments/suggestions
    Record the corrected information in the resolution box
Notes: Query Notification: The study coordinator will receive a query from the core lab asking for clarification/resolution of any issues that may arise with a study. It could be an incorrect date, subject ID or media issue. Review the variable name, reported value and comments/suggestions. Record the corrected information in the resolution box

## Slide 17: CMR Data Clarification Process Continued
  Media Queries
    Review the issue and comments/suggestions
    Record the corrected information and/or comments of action taken (Example: Sent Imaging Core new images via AG Mednet)
    Please print your name, sign and date (DD/MMM/YYYY) in the space provided. The Core Lab will not consider corrections recorded on the DCF unless signed and dated by site personnel completing the form. A signature indicates agreement that the data should be changed as indicated on the DCF.
  Questions ?
    Contact an Imaging Core Team Member for assistance
Notes: Show SLIDE and say--For any questions regarding a query, contact an imaging core team member for assistance.

## Slide 18: CMR Data Clarification Process Con’t
Resolution and Return of DCF
  The study center contact person must fax the completed DCF to the Imaging Core within five business days at 1-216-445-4419. The study center will keep a copy of the DCF with corresponding study files.
Unresolved Query Process
  If the Imaging Core does not receive the faxed resolution, a follow up email will be sent to the site study coordinator, and the DCC will be copied, for immediate attention/resolution of the DCF.
Notes: The study coordinator will fax the completed DCF to the Imaging Core within 5 business days, retaining a copy of the DCF with corresponding study files. . Unresolved queries may require sponsor involvement.

## Slide 19: Replacement/Inactivation Process
Imaging Core will initiate query to both site and DCC asking for clarification. Imaging Core will not process clarification received from site until sponsor (DCC) verifies the accuracy with signature on inactivation form.
  Site monitor or designee will verify the date and subject ID on the Inventory/Quality Report to ensure accuracy.
  Imaging Core will update the Inventory/Quality Report, PACS system and C5Research Clinical Data Management.
Notes: Replacements or inactivations can occur for many reasons –an example might be a subject’s study is sent to core lab and the subject is enrolled in another trial. Imaging Core will initiate query to both site and DCC asking for clarification. Imaging Core will not process clarification received from site until sponsor (DCC) verifies the accuracy with signature on inactivation form.

## Slide 20: CMR Contraindications
Heart rate > 120
Atrial fibrillation or irregular heart rate due to frequent ectopy
Brain aneurysm clips or vascular clips (titanium or titanium alloy are acceptable)
Cochlear implants
PPM/ICD
Insulin pumps
Any metallic fragment or foreign body (metal shrapnel or bullets)
Pregnant women
Breast tissue expanders
Aortic stent grafts
Indwelling pulmonary artery catheter – (follow center’s protocol)
Chronic Kidney Disease with GFR < 30 mL/min or known Gadolinium allergy are excluded from IV contrast, but can be enrolled for non-contrast CMR
Patients with uncontrollable severe claustrophobia
Patients in decompensated heart failure or with significant pleural effusions (moderate or more)
Patients unable to hold their breath for 10 – 15 sec
20
Notes: This list of contraindications can be found in the PVDOMICS MOP but I wanted to highlight chronic kidney disease with GFR
< 30 or known Gadolinium allergy. These subjects are excluded from IV contrast, but can be enrolled for non-contrast CMR exam

## Slide 21: Exceptions to Contraindications
CMR is safe with:
  Coronary stents
  Joint replacements
  ASD/PFO closure devices
  Sternal wires
  Most prosthetic heart valves
Notes: These are the exceptions to contraindications

## Slide 22: Getting Started
Secure the study assigned subject ID from the site coordinator
  In the system ID last name field, type PVD. In the MRN field type: Site ID (2 digits) and Subject ID (4 digits) for a 6 digit subject identifier- followed by Alpha characters (2) assigned by the DCC. Ex: 110002-AB. Please do not use subject names or initials to label the exam.
Notes: To get started, be certain to secure the study assigned subject ID from the site coordinator. If MRIs are not standard of care follow the above de-identification schema.

## Slide 23: CMR Image Acquisition
Acquire images according to the parameters described in the PVDOMICS Cardiac MRI Manual of Procedures
  Use consistent imaging parameters
  Subject positioning and plane orientations must remain consistent throughout the study
Be certain to use only the qualified MRI system
Notes: READ SLIDE

## Slide 24: MRI Protocol
Cardiac Structure/Function
Valvular Flow
Rest Perfusion Imaging
Optional imaging:
Pre-contrast MOLLI
Pulmonary artery compliance/remodeling
DHE – Myocardial Scar
Optional imaging:
4D flow
Optional imaging:
Post-contrast MOLLI
CMR Technique
Time
0
10
15
20
30
45
50
24
Notes: This is an estimated time line for image acquisition. The entire image acquisition should take approximately 50 minutes.

## Slide 25: Image Acquisition Instructions
Acquire images using consistent imaging parameters. Subject positioning and plane orientations must remain consistent throughout the study.
All subjects will be examined in the supine position.
EKG monitoring will be performed; lead placement is critical. Poorly placed leads result in blurred images and inaccuracies in data. Breath holding must be consistent. Placement of slices can be off as much as 2 cm when inconsistency with breath holds occurs.
Three-plane scout
Localizer: Axial single-shot blood (HASTE) images through the chest
8 mm thick, spaced to cover the aortic arch through the diaphragm
Acquisition during breath-hold is optimal for accuracy.
Localizer: Axial bright blood images through the chest
Single-shot SSFP
8 mm thick slices, spaced to cover the aortic arch through diaphragm
SSFP cine imaging (3 orientations)
Vertical long-axis orientation (2 chamber)
Horizontal long-axis orientation (4 chamber)
Left ventricular outflow tract (LVOT) orientation (3 chamber view)
Notes: These image acquisition instructions are found in the PVDOMICS MOP.

## Slide 26: Image Acquisition Instructions Continued
Common sequence parameters for cine imaging
8-mm slice thickness
2.3 mm minimum spatial resolution (for both phase and frequency encoding directions)
25-35 ms temporal resolution preferred; can be obtained by dropping views per segment captured between R to R intervals.
CMR with Late Gadolinium Enhancement (LGE)
Delayed short axis and long axis views should match slice locations of SSFP cine images. Copying the slice location is an industry standard. Cine images can be ordered to select the end diastolic trigger time by simply scrolling through a short axis image slice location. The selected time for end diastole can be entered into the actual trigger delay time prior to acquiring the delayed image set. This will enable a more accurate representation of the tracing to copy.
Notes: Remember that the delayed short axis and long axis views should match slice locations of SSFP cine images.

## Slide 27: Imaging Core Contact Information
Research Coordinator II
Cathy McDowell, BSW
Office: 216-445-7842 or 1-800-223-2273 ext. 57842
Fax: 216-445-4419
Email: mcdowec@ccf.org
Research Coordinator
Dawn D’Eusanio, BA
Office: 216-444-8267
Fax: 216-445-4419
Email: deusand@ccf.org
Project Specialist
Jill Rusticelli
Office: 216-442-5231
Fax: 216-445-4419
Email: rusticj@ccf.org
Project Specialist
Michelle Baksar
Office: 216-444-9872
Fax: 216-445-4419
Email: baksarm@ccf.org
Notes: Imaging Core Lab Contact Information can be found on these two slides.

## Slide 28: Imaging Core Contact Information Continued
Imaging Specialist:
Margaret (Koko) Park, BS, ACS, RDCS, RVT, FASE
Office: 216-445-5175
Fax: 216-445-4419
Email: parkm@ccf.org
Project Manager:
Kathy Kassimatis, RDCS, FASE
Office: 216-445-5156
Fax: 216-445-4419
Email: kassimk@ccf.org
Imaging Specialist:
Jeanne Drinko, RDCS, RCS, FASE
Office: 216-445-5274
Fax: 216-445-4419
Email: drinkoj@ccf.org
Core Lab Manager:
Annitta Flinn, BA, RDCS, CCRC, FASE
Office: 216-445-7673 or 1-800-223-2273 ext. 57673
Fax: 216-445-4419
Email: flinna@ccf.org
Notes: SKIP verbiage

## Slide 29: Quick Print Imaging Core Contact Information
AG Mednet Support | support@agmednet.com | 1-888-9246336
PVDOMICS DCC Website | http://qhsapps.ccf.org/pvdomics/
Notes: For your convenience we’ve provided a Quick Print Contact sheet for the Core Lab, AG Mednet Support and PVDOMICS DCC Website.

## Slide 30: References
American College of Radiology—North American Society for Cardiovascular Imaging Society for Pediatric Radiology Practice Parameter for the Performance and Interpretation of Cardiac Magnetic Resonance Imaging (MRI). Amended 2014 (Resolution 39)*).
ACCF/ACR/AHA/NASCI/SCMR, 2010 Expert Consensus Document on Cardiovascular Magnetic Resonance. Journal of the American College of Cardiology Vol 55, No. 23, 2010
Notes: THANK YOU for YOUR ATTENTION.

## Slide 31
Thank You!
Notes: We look forward to working with you soon on this exciting trial